## Slide 1: Comparative Evaluation of Feature Reduction Techniques for Intrusion Detection on IoMT Edge Devices
Yaoquan Ma(25298835), Wang Ning(25298832)
Supervisor: Dr. Priyanka Verma

## Slide 2
CONTENTS
Introduction
01
Related Work and Contribution
02
System Assumptions and Proposed Approach
03
Workflow and Technical Detail
04
Results
05
06
Google Docs QRCode
07
Conclusion and Future Work

## Slide 3
Background
IoMT enables continuous healthcare monitoring and supports modern medical services.
However, the increasing number of connected devices significantly expands the attack surface.
Motivation
Although AI-based IDS can strengthen security, limited computation, memory, storage, and bandwidth make direct deployment on IoMT edge devices challenging.
Cloud-based and hybrid AI-based IDS may introduce significant communication overhead, making efficient deployment strategies and feature processing methods important to study.
Introduction
Notes: Here I introduce the background and motivation of our study.
First, IoMT enables continuous healthcare monitoring and supports modern medical services. However, as the number of connected devices increases, the attack surface also becomes larger.
Second, although AI-based IDS can strengthen security, direct deployment on IoMT edge devices is still challenging because these devices have limited computation, memory, storage, and bandwidth.
In addition, cloud-based and hybrid AI-based IDS may introduce significant communication overhead. Therefore, it is important to study efficient deployment strategies and feature processing methods. This is the main motivation of our work.

## Slide 4
Research Gaps and Contributions
GAP 1
Gap 1 — Accuracy-Oriented Research
Existing edge-based, cloud-based, and hybrid IDS studies mainly focus on improving detection accuracy, with limited evaluation of whether the resource demands are practical for edge devices.
Contribution 1
We extend the evaluation beyond accuracy by assessing CPU, memory, and network overhead under resource-constrained deployment settings.
GAP 2
GAP 2 — Unresolved Transmission Overhead
In cloud-based and hybrid settings, large volumes of flow-level features, logs, and events may need to be uploaded, yet few studies evaluate how to reduce this transmission cost or whether the edge can sustain the resulting overhead.
Contribution 2
We simulate split deployment between the edge and the cloud, and evaluate whether edge-side feature extraction can reduce traffic while keeping the resource overhead manageable.
Contribution 1 — Deployment-Aware Evaluation
Contribution 2 — Edge–Cloud Split Assessment
Notes: First, many existing IDS studies focus mainly on accuracy improvement, but they often do not evaluate whether the resource cost is practical for edge devices. So, our first contribution is to evaluate not only accuracy, but also CPU, memory, and network overhead.
Second, in cloud-based and hybrid settings, a large amount of data may need to be uploaded, including flow-level features, logs, and events. However, only limited work studies how to reduce this transmission cost or whether the edge can support it. So, our second contribution is to simulate edge–cloud split deployment and examine whether edge-side feature extraction can reduce traffic with acceptable overhead

## Slide 5
Related work
03
Hybrid Framework
02
Lightweight ML
Keeps raw data local and protects privacy by sharing model updates instead of patient data.
01
Federated Learning
Focus
Focus
Focus
Limitation
Still requires repeated local training and multiple communication rounds, which remain costly for resource-constrained IoMT devices.
Limitation
Many studies assume that “lightweight” means deployable, but do not systematically evaluate real CPU or memory overhead, and often remain in edge-only settings.
Existing hybrid work often improves accuracy, but lacks clear evaluation of network overhead, split deployment cost, and practical feasibility.
Uses smaller models to make edge-side intrusion detection more feasible under limited resources.
Combines lightweight edge processing with stronger cloud-side analysis to balance efficiency and detection capability.
Limitation
Representative refs: Ghourabi and Alkhalil (2025); Popoola et al. (2022); Chen et al. (2020)
Representative refs: Ali et al. (2025); Doriguzzi-Corin et al. (2020); Kalakoti et al. (2022)
Representative refs: Wu et al. (2025); Rguibi et al. (2025); Huma et al. (2021)
Notes: The first direction is Federated Learning. Its main focus is to protect privacy by keeping raw data on local devices and sharing model updates instead of patient data. However, it still requires repeated local training and multiple communication rounds, which can be costly for resource-constrained IoMT devices.
The second direction is Lightweight ML. It uses smaller models to make edge-side intrusion detection more feasible. But many studies assume that lightweight means deployable, while they do not carefully evaluate real CPU or memory overhead.
The third direction is Hybrid Framework. It combines lightweight edge processing with stronger cloud-side analysis. This is a promising direction, but existing work still lacks clear evaluation of network overhead, split deployment cost, and practical feasibility.

## Slide 6: Methodology: System Overview
Feature Selection
Feature encoding
Feature Selection
Feature encoding
Feature Selection
Feature encoding
IoMT-Based Wearable Devices
Edge Computing layer
Feature Selection
Feature encoding
…..
AI + IDS
Firewall
Load Balance
Storage
Servers
Network
flow-level, logs, event
medical sensitive data
Cloud layer
Alter, Security policy
Healthcare
Professional
Security Operator
Notes: This slide presents the overall system architecture of our framework.
The whole framework can be understood in three layers: the IoMT device layer at the bottom, the edge computing layer in the middle, and the cloud layer at the top.
At the bottom, we have IoMT-based wearable devices. These devices continuously generate both medical data and network-related data. Because they are resource-constrained, we do not place the full intrusion detection task directly on them.
In the middle is the edge computing layer. Here, the system mainly performs lightweight operations, such as feature encoding and feature selection. The edge also has some basic blocking capability, so it can react to simple suspicious behaviour. However, it may not recognise more advanced or complex attacks.
For this reason, the edge keeps sending flow-level features, logs, and events to the cloud. In the cloud layer, the AI-based IDS performs the main classification and deeper security analysis, because the cloud has stronger computation, storage, and network resources.
When the cloud identifies a complex attack, it sends the result or security policy back to the edge. Then the edge uses this information to block the attack locally. So, the cloud is mainly responsible for advanced detection, while the edge is responsible for lightweight processing, reporting, and local enforcement.
On the left side, the Security Operator represents the security management role. This means alerts and security policies can be reviewed and adjusted through the cloud system.
On the right side, the figure highlights the healthcare context of the framework. The uploaded information may include medical sensitive data, so the system is not only protecting network traffic, but also protecting healthcare-related data and services. The Healthcare Professional represents the real application side that depends on this secure system.

## Slide 7: Methodology: Proposed Simulation Framework
DataSet
Feature extraction
PCA, AutoEncoder, ResNeXt
Feature Selection
Feature scaling
Classifer Model
Feature Encoding
Classification result
attack
attack
attack
normal
Test
Train
Network traffic
CPU
Memory
Accuracy
F1 score
Edge Simulation
Cloud Simulation
Test
Train
1
2
3
5
4
Notes: In our implementation, we conduct experiments on an ARM platform to simulate a realistic edge environment. To ensure fairness and reflect real-world constraints, we do not use GPU acceleration or MPS, and all computations are performed on CPU.
Since we evaluate a hybrid framework, we simulate both edge and cloud components.
In the edge simulation, we first read data from the dataset, then apply feature scaling and feature selection to remove redundant or less informative features. After that, we perform feature extraction using methods such as PCA, AutoEncoder, or ResNeXt, and transmit the processed features to the cloud.
On the cloud side, the received data is reshaped based on metadata and then split into training and testing datasets. The data is then fed into a classification model for training and evaluation.
Finally, the classification results can be used to generate alerts or trigger defence strategies.
During this process, we monitor and record CPU and memory usage at the edge during feature extraction, as well as network traffic. We also evaluate model performance using metrics such as accuracy and F1 score.

## Slide 8: Methodology: Dataset & Feature Reduction technique
Edge-IIoTset (2022)
  Realistic edge-based IoT traffic
  Labelled data (normal vs. attack)
  Suitable for IDS evaluation in edge environments
  Recent dataset reflecting modern traffic patterns
  flow-level data
Feature Reduction Technique
  Feature Selection (manual/statistical)
  PCA (traditional dimensionality reduction)
  Autoencoder
  ResNeXt1D (deep representation)
Notes: In terms of we use the Edge-IIoTset dataset, which is a recent dataset designed for edge-based IoT environments(publish in 2022). It contains realistic network traffic and includes labelled data for both normal and attack behaviours, making it suitable for evaluating intrusion detection systems. In addition, the data is provided at the flow level, which aligns well with our system design and reduces computational complexity.
For feature reduction, we investigate several approaches. First, we apply feature selection methods based on feature value ranges and their importance for prediction, in order to remove redundant or less informative features. Then, we use PCA as a traditional dimensionality reduction technique to project the data into a lower-dimensional space. Finally, we explore deep learning-based methods, including AutoEncoder and ResNeXt1D, to learn more complex feature representations.
The main objective is to reduce the number of features while preserving the most important information, so that we can improve efficiency without significantly reducing classification performance.

## Slide 9: Methodology: Dataset & Feature Reduction technique
ResNeXt1D Feature Extraction
Reshape input
Transform X from [N, D] to [N, 1, D]
Pass batch through stem layer
- Conv1D(1 → 64, kernel=4, stride=2, padding=3)
- BatchNorm1D
- ReLU
- MaxPool1D(kernel=3, stride=2, padding=1)
Pass through Layer 1 and Layer 2
- ResNeXt1D Block
- ResNeXt1D Block
Pass through head
- Adaptive Average Pooling
- Flatten
- Linear layer to embedding_dim
Output: Embedding matrix Z (n × embedding_dim)
AutoEncoder Feature Extraction
Input: Flow-level data X (n × d)
Pass X through the encoder
- Linear (36->64)
- ReLU
- Linear (64->32)
- ReLU
Encode X into low-dimensional latent vectors
- Linear (32 -> embedding_dim)
Output: Embedding matrix Z (n × embedding_dim)

## Slide 10: Results: Detection Performance

## Slide 11: Results: Detection Performance

## Slide 12: Results: Detection Performance

## Slide 13: Conclusion
Feature reduction techniques, including PCA, AutoEncoder, generally lead to a decrease in model performance, particularly in terms of accuracy and F1 score.
If a certain degree of performance degradation is acceptable, more aggressive dimensionality reduction can be applied to significantly reduce feature size and computational cost.
ResNeXt introduces high CPU overhead when applied to low-dimensional flow-level data, without improving accuracy or F1 score, making it unsuitable for deployment on edge devices. In contrast, PCA and AutoEncoder show no significant resource bottlenecks and are more suitable for edge-based IDS.
Feature reduction reduces performance but improves efficiency; PCA and AutoEncoder are edge-friendly, while ResNeXt is computationally expensive and ineffective for low-dimensional data.

## Slide 14: References
IoMT Security Papers
IDS and ML/DL Papers
Feature Reduction Techniques
Relevant academic sources